## Slide 1
فرکانس میکروکنترلر: freq 8000000
تعداد باود در هر ثانیه: baudRate 1225
تعداد دور هر فرکانس بالا در یک ثانیه: highFreq 7350
تعداد دور هر فرکانس پایین در یک ثانیه: lowFreq 4900
rx_buf_size 32
timer_clock_select 3
زمان هر دور تایمر 2 بر حسب میکروثانیه: micros_per_timer_count 8 / (freq / 1000000) = 8r / (8000000r/s / 1000000µ) = 8r / 8r/µs = 1µs/r
زمان هر باود بر حسب میکروثانیه: bit_period 1000000 / baudRate = 1000000µ / 1225b/s = 816µs/b
زمان هر دور فرکانس بالا برحسب میکروثانیه: high_freq_micros 1000000 / highFreq = 1000000µ / 7350r/s = 136µs/r
زمان هر دور فرکانس پایین بر حسب میکروثانیه: low_freq_micros 1000000 / lowFreq = 1000000µs / 4900r/s = 204µs/r
تعداد دور فرکانس بالا در هر باود: high_freq_cnt bit_period / high_freq_micros = 816µs/b / 136µs/r = 6r/b
تعداد دور فرکانس پایین در هر باود: low_frec_cnt bit_period / low_freq_micros = 816µs/b / 204µs/r = 4r/b
تعداد دوری که تایمر 2 در هر باود میزند: tcnt_bit_period bit_period / micros_per_timer_count = 816µs/b / 1µs/r = 816r/b
نسبت زمان هر دور فرکانس بالا به زمان هر دور تایمر 2: tcnt_high_freq high_freq_micros / micros_per_timer_count = 136µs/r / 1µs/r = 136
نسبت زمان هر دور فرکانس پایین به زمان هر دور تایمر 2: tcnt_low_freq low_freq_micros / micros_per_timer_count = 204µs/r / 1µs/r = 204
tcnt_high_th_l tcnt_high_freq - (tcnt_low_freq - tcnt_high_freq) / 2 = 136 - 34 = 102
tcnt_high_th_h tcnt_high_freq + (tcnt_low_freq - tcnt_high_freq) / 2 = 136 + 34 = 170
tcnt_low_th_l tcnt_low_freq – (tcnt_low_freq - tcnt_high_freq) / 2 = 204 - 34 = 170
tcnt_low_th_h tcnt_low_freq + (tcnt_low_freq - tcnt_high_freq) / 2 = 204 + 34 = 238
816µs
136µs
204µs
CS12 | CS11 | CS10 | Description
0 | 0 | 0 | No clock source (Timer/Counter stopped)
0 | 0 | 1 | clk
0 | 1 | 0 | clk/8
0 | 1 | 1 | clk/64
1 | 0 | 0 | clk/256
1 | 0 | 1 | clk/1024
1 | 1 | 0 | External clock source on T1 pin. Clock on falling edge.
1 | 1 | 1 | External clock source on T1 pin. Clock on rising edge.
TCCR1B – Timer/Counter Control Register B |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
ICNC1 | ICES1 | - | WGM13 | WGM12 | CS12 | CS11 | CS10
W | W | R | R | R/W | R/W | R/W | R/W
High
Low

## Slide 2
// Analog comparator interrupt
ISR(ANALOG_COMP_vect)
{
SoftModem::activeObject->demodulate();
}
void SoftModem::demodulate(void)
{
  uint16_t t = TCNT1;
  uint16_t diff;
  diff = t - _lastTCNT;
  if (diff < tcnt_high_th_l)
  return;
  _lastTCNT = t;
  if(diff > tcnt_low_th_h)
  return;
  if(tcnt_low_th_l <= diff && diff <= tcnt_low_th_h)
  {
  _lowCount += diff;
    if(_recvStat == INACTIVE)
    {
      // Start bit detection
      if(_lowCount >= tcnt_bit_period * 0.5)
      {
        _recvStat = START_BIT;
        _highCount = 0;
        _recvBits = 0;
        OCR1A = t + tcnt_bit_period - _lowCount;
        TIFR |= (1<<OCF1A);
        TIMSK |= (1<<OCIE1A);
      }
    }
  }
  else if(tcnt_high_th_l <= diff && diff <= tcnt_high_th_h)
  {
    if(_recvStat == INACTIVE)
    {
      _lowCount = 0;
      _highCount = 0;
    }
    else
    {
    _highCount += diff;
    }
  }
}
TCNT1 – Timer/Counter Register |  |  |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
TCNT1H[15:8] |  |  |  |  |  |  | 
R/W | R/W | R/W | R/W | R/W | R/W | R/W | R/W
OCR1A – Output Compare Register A |  |  |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
OCR1AH[15:8] |  |  |  |  |  |  | 
R/W | R/W | R/W | R/W | R/W | R/W | R/W | R/W
TIFR – Timer/Counter Interrupt Flag Register |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OCF2 | TOV2 | ICF1 | OCF1A | OCF1B | TOV1 | OCF0 | TOV0
R/W | R/W | R/W | R/W | R/W | R/W | R/W | R/W
TIMSK – Timer/Counter Interrupt Mask Register |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OCIE2 | TOIE2 | TICIE1 | OCIE1A | OCIE1B | TOIE1 | OCIE0 | TOIE0
R/W | R/W | R/W | R/W | R/W | R/W | R/W | R/W
High
Low
136 – 34 = 102
136 + 34 = 170
204 – 34 = 170
204 + 34 = 238
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
TCNT1L[7:0] |  |  |  |  |  |  | 
R/W | R/W | R/W | R/W | R/W | R/W | R/W | R/W
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OCR1AL[7:0] |  |  |  |  |  |  | 
R/W | R/W | R/W | R/W | R/W | R/W | R/W | R/W

## Slide 3
// Timer 2 compare match interrupt A
ISR(TIMER1_COMPA_vect)
{
  OCR1A += Modem::activeObject->tcnt_bit_period;
  Modem::activeObject->recv();
}
void Modem::recv(void)
{
  uint8_t high;
  // Bit logic determination
  if(_highCount > _lowCount)
  {
    _highCount = 0;
    high = 0x80;//0b1000 0000
  }
  else
  {
    _lowCount = 0;
    high = 0x00;//0b0000 0000
  }
  // Start bit reception
  if(_recvStat == START_BIT)
  {
    if(!high)
    {
    _recvStat++;
    }
    else
    {
    goto end_recv;
    }
  }
  // Data bit reception
  else if(_recvStat <= DATA_BIT)
  {
    _recvBits >>= 1;
    _recvBits |= high;
    _recvStat++;
  }
  // Stop bit reception
  else if(_recvStat == STOP_BIT)
  {
    if(high)
    {
    // Stored in the receive buffer
      uint8_t new_tail = (_recvBufferTail + 1 == rxBufSize) ? 0 : _recvBufferTail + 1;
    if(new_tail != _recvBufferHead)
    {
        *(_recvBuffer + _recvBufferTail) = _recvBits;
    _recvBufferTail = new_tail;
    }
    else
    {
    ;// Overrun error detection
    }
    }
    else
    {
    ;// Fleming error detection
    }
  goto end_recv;
  }
  else
  {
end_recv:
  _recvStat = INACTIVE;
  TIMSK &= ~(1<<OCIE1A);
  }
}
int Modem::available()
{
return (_recvBufferTail + rxBufSize - _recvBufferHead) & (rxBufSize - 1);
}
int Modem::read()
{
  if(_recvBufferHead == _recvBufferTail)
  return -1;
  int d = _recvBuffer[_recvBufferHead];
  _recvBufferHead = (_recvBufferHead + 1) & (rxBufSize - 1);
  return d;
}
Low
Start bit
High
Data bit
High
Data bit
High
Data bit
Low
Data bit
High
Data bit
High
Data bit
Low
Data bit
Low
Data bit
High
Stop bit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
_recvBufferHead
_recvBufferTail
TIMSK – Timer/Counter Interrupt Mask Register |  |  |  |  |  |  | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OCIE2 | TOIE2 | TICIE1 | OCIE1A | OCIE1B | TOIE1 | OCIE0 | TOIE0
R/W | R/W | R/W | R/W | R/W | R/W | R/W | R/W
OCR1A – Output Compare Register A |  |  |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
OCR1AH[15:8] |  |  |  |  |  |  | 
R/W | R/W | R/W | R/W | R/W | R/W | R/W | R/W
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OCR1AL[7:0] |  |  |  |  |  |  | 
R/W | R/W | R/W | R/W | R/W | R/W | R/W | R/W

## Slide 4
onsubmit="generate($('data').value)
function $(name)
{
return document.getElementById(name);
}
function generate(str)
{
if (str.length == 0) return;
var utf8 = toUTF8(str);
console.log(utf8);
var sampleRate = 29400;
var baud = 1225;
var freqHigh = 7350;
var freqLow = 4900;
var spb = sampleRate / baud; // 24 samples per bit
var preCarrierBits = Math.ceil(sampleRate * 40 / 1000 / spb); // 49 bits
var postCarrierBits = Math.ceil(sampleRate * 5 / 1000 / spb); // 6.125 bits => 7 bits
var size = (preCarrierBits + postCarrierBits + 10 * utf8.length) * spb;
var data = "RIFF" + chr32(size + 36) + "WAVE" + "fmt " + chr32(16, 0x00010001, sampleRate, sampleRate, 0x00080001) + "data" + chr32(size);
function pushData(freq, samples)
{
for (var i = 0; i < samples; i++)
{
var v = 128 + 127 * Math.sin((2 * Math.PI) * (i / sampleRate) * freq);
data += chr8(v);
}
}
pushData(freqHigh, preCarrierBits * spb);
for (var x in utf8)
{
var c = (utf8[x] << 1) | 0x200;
for (var i = 0; i < 10; i++ , c >>>= 1)
pushData((c & 1) ? freqHigh : freqLow, spb);
}
pushData(freqHigh, postCarrierBits * spb);
if (size + 44 != data.length) alert("wrong size: " + size + 44 + " != " + data.length);
dataURI = "data:audio/wav;base64," + escape(btoa(data));
audio = new Audio(dataURI);
audio.play();
$('jmp').disabled = false;
}
function toUTF8(str)
{
var utf8 = [];
for (var i = 0; i < str.length; i++)
{
var c = str.charCodeAt(i);
if (c <= 0x7f)
utf8.push(c);
else if (c <= 0x7ff)
{
utf8.push(0xc0 | (c >>> 6));
utf8.push(0x80 | (c & 0x3f));
}
else if (c <= 0xffff)
{
utf8.push(0xe0 | (c >>> 12));
utf8.push(0x80 | ((c >>> 6) & 0x3f));
utf8.push(0x80 | (c & 0x3f));
}
else
{
var j = 4;
while (c >>> (6 * j))
j++;
utf8.push(((0xff00 >>> j) & 0xff) | (c >>> (6 * --j)));
while (j--)
utf8[idx++] = 0x80 | ((c >>> (6 * j)) & 0x3f);
}
}
return utf8;
}
data:audio/wav;base64,